'Initialise 'Start program

   Dim Portcpinsdirection As Byte 'To Setup Port C
   Dim Adclowbyte As Byte 'Accelerator input low byte
   Dim Adchighbyte As Byte 'Accelerator input high byte
   Dim Acceleratorvalue As Word 'Accelerator input word
   Dim Numberofbatteries As Word 'Number of batteries demanded by accelerator input
   Dim Rotatetimer As Integer 'To set the time it takes before the battery bank starting point is incremented
   Dim Batterybankstartingpoint As Integer 'To indicate which battery is the starting point
   Dim Switchesbatteryinpositions As Word 'To indicate which of the switches must insert their battery and not bypass.
   Dim B As Word 'Used in the process to calculate the new battery bank starting point.B is used as tempory storage for Switchesbatteryinpositions
   Dim H As Integer 'H is used to count the number of battery posisions needed to shift the starting point
   Dim Switchesbatteryinpositionsold As Word 'Save Switchesbatteryinpositions to compare it to the new Switchesbatteryinpositions during the next program loop
   Dim Batterycontrol As Byte 'The byte that will be send via port B, D or C to switch in or out the required batteries.
   Dim Checkbitnew As Bit 'Used to determine individual Bit Status of Switchesbatteryinpositions
   Dim Checkbitold As Bit 'Used to determine individual Bit Status of Switchesbatteryinpositionsold
   Dim N As Integer 'Used to step through 10 battery positions
   Dim L As Word 'Used to ensure that switches increment only one battery at a time when going up or down
   Dim Q As Word 'Used as a tempory storage for L

'Configure the external ports

   Config Portb = Output 'LSBits of Switches Battery-In Positions
   Config Portd = Output 'LSBits of Switches Bypass Positions
   Portcpinsdirection = &B1111 'PortC Pins 0 to 3 are used as outputs.
   Out &H34 , Portcpinsdirection 'Use pin 0 and 1 for MSBits of Switches Battery-In Positions together with Port B
        'Use pin 2 and 3 for MSBits of Switches Bypass Positions together with Port D

'Set the initial values of variables to zero

   Rotatetimer = 0
   Batterybankstartingpoint = 0
   H = 0
   B = 0
   Switchesbatteryinpositionsold = &B0000000000
   N = 0
   L = 0
   Q = 0
   Out &H38 , &B00000000
   Out &H35 , &B0000
   Out &H32 , &B00000000

   Delay

Start:

'Read Accelerator

   Out &H27 , &B00000101 'Setup the Adc - Port ADC5
   Out &H26 , &B11010111

   Adclowbyte = Inp(&H24) 'Read Accelerator
   Adchighbyte = Inp(&H25)
   'Adclowbyte = &B00100000 'Note: For simulation only
   'Adchighbyte = &B00000000

   Delay

   Acceleratorvalue = Makeint(adclowbyte , Adchighbyte) ' 'Combine ADC bytes into a word for eveluation
      If Acceleratorvalue <= &B10111 Then Numberofbatteries = &B0 ' 'Determine accelerator position and set output value
      If Acceleratorvalue >= &B11000 Then Numberofbatteries = &B1
      If Acceleratorvalue >= &B1111100 Then Numberofbatteries = &B11
      If Acceleratorvalue >= &B11100000 Then Numberofbatteries = &B111
      If Acceleratorvalue >= &B101000100 Then Numberofbatteries = &B1111
      If Acceleratorvalue >= &B110101000 Then Numberofbatteries = &B11111
      If Acceleratorvalue >= &B1000001100 Then Numberofbatteries = &B111111
      If Acceleratorvalue >= &B1001110000 Then Numberofbatteries = &B1111111
      If Acceleratorvalue >= &B1011010100 Then Numberofbatteries = &B11111111
      If Acceleratorvalue >= &B1100111000 Then Numberofbatteries = &B111111111
      If Acceleratorvalue >= &B1110011100 Then Numberofbatteries = &B1111111111
      If Acceleratorvalue >= &B10000000000 Then Numberofbatteries = &B0 ' 'Ensure default 0 for higher than 10 bit max ADC values

   Delay

   Q = L 'Store L
   If Numberofbatteries > L Then Shift L , Left , 1 'Ensure that switches increment one battery at a time when going up.
   If Numberofbatteries > Q Then Numberofbatteries = L + 1
   If Numberofbatteries < L Then Shift L , Right , 1 'Ensure that switches increment one battery at a time when going up
   If Numberofbatteries < Q Then Numberofbatteries = L
   L = Numberofbatteries

   Delay

'Set Battery Bank Rotation Indicators

   Rotatetimer = Rotatetimer + 1 ' 'Increment battery bank cycle/rotate timer
   If Rotatetimer = 1000 Then Batterybankstartingpoint = Batterybankstartingpoint + 1 'Test timer for maximum and set next battery starting piont
   If Rotatetimer = 1000 Then Rotatetimer = 0 ' 'Reset timer for next battery bank cycle increment
   If Batterybankstartingpoint = 10 Then Batterybankstartingpoint = 0 ' 'Reset battery bank starting piont to 0

   Delay

'Rotate the battery bank starting point

   Switchesbatteryinpositions = Numberofbatteries 'Store accelerator position
      For H = 1 To Batterybankstartingpoint 'Process new battery switches output word
      Shift Switchesbatteryinpositions , Left , 6
      B = Switchesbatteryinpositions
      Shift Switchesbatteryinpositions , Right , 15
      Shift B , Left , 1
      Shift B , Right , 6
      Switchesbatteryinpositions = Switchesbatteryinpositions Or B
      Next H

   Delay

'Compare previous switch-on position word with the new one - bit by bit

   For N = 0 To 9
   Checkbitnew = Switchesbatteryinpositions.n
   Checkbitold = Switchesbatteryinpositionsold.n
   If Checkbitnew > Checkbitold Then Gosub Kickright
   If Checkbitold > Checkbitnew Then Gosub Kickleft
   Next N
   N = 0
   Switchesbatteryinpositionsold = Switchesbatteryinpositions

Goto Start

'Bypass the battery position

Kickleft:
If N = 0 Then Batterycontrol = &B00000001
If N = 1 Then Batterycontrol = &B00000010
If N = 2 Then Batterycontrol = &B00000100
If N = 3 Then Batterycontrol = &B00001000
If N = 4 Then Batterycontrol = &B00010000
If N = 5 Then Batterycontrol = &B00100000
If N = 6 Then Batterycontrol = &B01000000
If N = 7 Then Batterycontrol = &B10000000
If N = 8 Then Batterycontrol = &B0100
If N = 9 Then Batterycontrol = &B1000
If N <= 7 Then Out &H32 , Batterycontrol
If N > 7 Then Out &H35 , Batterycontrol
Waitms 25
Out &H35 , &B0000
Out &H32 , &B00000000
Return

'Switch The Battery In

Kickright:
If N = 0 Then Batterycontrol = &B00000001
If N = 1 Then Batterycontrol = &B00000010
If N = 2 Then Batterycontrol = &B00000100
If N = 3 Then Batterycontrol = &B00001000
If N = 4 Then Batterycontrol = &B00010000
If N = 5 Then Batterycontrol = &B00100000
If N = 6 Then Batterycontrol = &B01000000
If N = 7 Then Batterycontrol = &B10000000
If N = 8 Then Batterycontrol = &B0001
If N = 9 Then Batterycontrol = &B0010
If N <= 7 Then Out &H38 , Batterycontrol
If N > 7 Then Out &H35 , Batterycontrol
Waitms 25
Out &H38 , &B00000000
Out &H35 , &B0000
Return

End